## Slide 1: Assignment 5.2 - Presentation
Leo Gipson Jr
Course Number: rbt125
Instructor’s Name: Prof. Matthew prater
Assignment Due Date: February 11th, 2024

## Slide 2: function of the Crowbar Circuit.
The main function of the Crowbar Circuit is to shutdown power output from a supply in the event the supply begins to exhibit overvoltage. As the name implies, it is like dropping a crowbar over an exposed power supply terminals. The operation puts a short circuit or low resistance path across the voltage output. The overvoltage or other fault conditions may arise due to operator error, a fault in either the load or the power supply. Due to the nature and sensitivity of the present day electronics and extremely low operational voltages, it is important to ensure that the safe voltages are not exceeded.

## Slide 3: Where is the Crowbar circuit used?
Active crowbars are commonly used to protect the frequency converter in the rotor circuit of doubly fed generators against high voltage and current transients caused by the voltage dips in the power network. The other commonly used crowbar device is the Gas Discharge Tube, (GDT) which is a miniature spark gap usually housed in a ceramic enclosure. When triggered by a high voltage, the spark gap conducts, and all current flow is diverted. Spark gaps can be manufactured such that they protect from modest voltages (around 100 V) to thousands of volts such as from lightning, When the overvoltage situation clears, the TSP or GDT goes back to normal, high-impedance mode. Several fault-conditions may lead to possible over voltages. These include a fault in either the power supply or the load, and operator error. Present day electronics are sensitive and often operate at very low voltages with small margin. That makes it imperative to ensure that the safe voltages are not exceeded, and sensitive and expensive equipment remain undamaged. Crowbars are used for HV tube (klystron and IOT) protection.

## Slide 4: Advantages of the CROWBAR circuit?
The advantage of a crowbar circuit is that the low holding voltage of the crowbar lets it carry higher fault current without dissipating much power in turn would otherwise cause overheating. Also, a crowbar is more likely than a clamp to deactivate a device (by blowing a fuse or tripping a breaker), bringing attention to the faulty equipment.

## Slide 5: Disadvantages of the CROWBAR circuit?
The overvoltage value of the circuit depends purely upon the Zener voltage value, and only few values of Zener diode are available. The circuit is also subjected to noise problems; this noise can often create a false trigger and blow up the fuse. In event of overvoltage the circuit blows the fuse and later requires manual help to run the load again when the voltage gets normal. The fuse is a mechanical fuse which must be replaced and hence consumes effort, time, and money. Recovery is only possible by manually replacing the fuse, once the fault condition is repaired. This is a time-consuming affair, and not helpful for low downtime appliances. Therefore, most engineers prefer a fold-back type of crowbar protection.

## Slide 6: Variations of the of the CROWBAR circuit?
A Crowbar Using Triac and SSB, which uses a SSB or a silicon bilateral switch, as the gate driver for the triac. The preset R2 is used for setting the triggering point of the SSB at which the device can fire and trigger ON the triac. This setting is done corresponding to the desired high voltage level at which the crowbar needs to trigger and protect the connected circuit from a possible burn out. As soon as the high voltage situation is reached, as per the R2 setting the SSB detects this over voltage, and it switches ON. Once it switch es ON it fires the triac. The triac instantly conducts and shorts circuits the line voltage which in turn causes the fuse to blow. Once the fuse blows, the voltage to the load is cut off and the danger of the over voltage is averted.
A Crowbar Circuit Using Triac and Zener Diode, the zener voltage decides the cut off limit of the crowbar circuit. In the figure it is shown as 270V, therefore as soon as the 270 V mark is reached, the zener starts conducting. As soon as the zener diode breaks over and conducts, the triac is switched ON. The triac switches ON and short circuits the line voltage thereby bowing off the fuse the preventing further dangers that may resulted in due to the high voltage.
A Crowbar Circuit Using SCR, a simple SCR transistor crowbar circuit which delivers over-voltage protection in case there is a malfunction of the voltage regulator for over-voltage protection or high level from an external source. It is supposed to be employed with a supply source that includes some type of short circuit protection, possibly fold-back current limiting or a basic fuse. The best possible application can be a 5V logic supply, because TTL could be quickly destroyed by too much voltage.

## Slide 7
references
Cadence. How Crowbar Circuits Work.
https://resources.pcb.cadence.com/blog/how-crowbar-circuits-work
Wikipedia Encyclopedia. Crowbar Circuit.
https://en.wikipedia.org/wiki/Crowbar_(circuit)
WestFlorida Components. Where would you apply crowbar protection?
https://www.westfloridacomponents.com/blog/apply-crowbar-protection/
Circuit Digest. Crowbar Circuit.
https://circuitdigest.com/electronic-circuits/crowbar-circuit-diagram
Fmuser. Three Main Types of Crowbar Circuits for Over-voltage Protection.
https://www.visualcapitalist.com/chart-evolution-standard-oil